## Slide 1: Delta V4 Access Control
Overview

## Slide 2
Delta Access Control Solution V3 Access
2 single direction doors or 1 bi-directional door
Up to twelve door modules may be connected to an ASM/eBMGR via LINKnet (RS-485)
built-in battery charging circuit
2
CPU provides local authentication & authorization
Controls up to twelve door modules via LINKnet (RS-485)
ASM
ADM-2W704

## Slide 3
Delta Access Control Solution O3 CPU
50,000
10,000
294/916
OSDP
Local authentication and authorization
anonymized access users (optional)
Multi-factor authentication
Confidential Property of Delta Controls Inc.

## Slide 4
Delta Access Control Solution O3 Access Module
Wiegand26, wiegand37, custom, GSA75
294
wiegand input
door contact, REX
door lock, cardreader LED
universal I/O
12V / 24V
single door

## Slide 5
Delta Access Control Solution O3 Modular Solution
The number of doors controlled by a single O3 can be extended to a max of 24 by connecting up to 5 Power Injectors
CAN bus
<= 70m
Max 4 modules
Max 4 modules

## Slide 6
Delta Access Control Solution O3 Modular Solution
distributed access control system with similar architecture to ASM & ADM

## Slide 7
Delta Access Control Solution O3 PoE Access (roadmap)
OSDP & wiegand
2 door (or 1 bidirectional)
802.3bt 60W (4P PoE)
12V / 24V
294
PoE install typically requires ½ time and resources
Battery backup at the switch

## Slide 8
Delta Access Control Solution O3 PoE Access Controller
  Simplified installation and wiring
  Saves on labor installation only CAT5/6 cable
  Battery backup at the server

## Slide 9
Delta Access Control Solution
Typical Single Direction Door
  1 - O3-DIN-ACCESS with 12/24 electric strike, card reader, door contact, and 12/24 request to exit device
Single Direction Door with holder
  1 - O3-DIN-ACCESS with 12/24 electric strike, card reader, door contact, and 12/24 request to exit device, and 12/24VDC door holder

## Slide 10
Delta Access Control Solution
Synchronization engine (V3 & V4)
Master database
Fault-tolerant
Event log

## Slide 11: Access Control V4: Access Dashboard
A customizable intuitive dashboard for non-technical users
Delta Access Control Solution eWEB Access Dashboard

## Slide 12
Role based permissions make enrolling a new user simple and intuitive
The permissions for each user are customizable
Delta Access Control Solution eWEB Access Dashboard

## Slide 13
Powerful search capabilities
Intuitive visualization
Delta Access Control Solution eWEB Access Dashboard

## Slide 14
A responsive design means the dashboard can be used on different types of devices
Delta Access Control Solution eWEB Access Dashboard

## Slide 15
Delta Access Control Solution eWEB Access Widgets

## Slide 16
Delta Access Control Solution BACnet Secure Connect (BACnet/SC)
Digital certificates
TLS encryption
Public/private keys infrastructure